## Slide 1
Inter Integrated Circuit Bus Protocol
(I2C)
By:
Harekrishna ray
Neel Pambhar
Ayushi Gajera

## Slide 2
I2C bus => Philips, consumer products (TV)
Originally intended for operation on one single board (PCB)
Today, variety of devices are available with on-chip I2C interface. i.e. Microcontroller, E2PROM, A/D converters etc.

## Slide 3: I2C Bus Terminology
Term | Description
Transmitter | Device which send data to bus
Receiver | Device which receives data from bus
Master | Device which initiates transfer, generate CLK signal to permit data transfer and stop data transfer
Slave | Device addressed by Master
Multi-Master | More than one Master control bus at same time
Arbitration | Procedure to allow one Master among Multi-Master, whose message is not corrupted

## Slide 5: I2C Bus Characteristics
Two wires, SDA, SCL carry information between devices connected on bus
Every device hooked on the bus is identified by unique address (7-bit slave address)
Synchronous, Half-duplex serial communication
Unique Start and Stop conditions

## Slide 6
Acknowledgement after each transferred byte
Improves reliability of communication
Multi-Master Capability
Bi-directional data transfer
No chip enable (Slave Select Signal, SPI) is required.

## Slide 7: Realization

## Slide 8: DATA Transfer on the I2C Bus
In normal data transfer, the data line (SDA) only changes state when the clock (SCL) is low.
SDA
SCL
Data line stable; Data valid
Change of data allowed

## Slide 9: Start and Stop Conditions
A transition on the data line while the clock line is high is defined as either a start or a stop condition.
Both start and stop conditions are generated by the bus master
The bus is considered busy after a start condition, until a stop condition occurs
Start Condition
Stop Condition
SCL
SCL
SDA
SDA

## Slide 10: Addressing Scheme
Every devices, hook up on bus=> own unique address.
Master => 7-bit address => device which it want to access.
After START condition, 7-bit address sent along with data direction bit (R/W’)
Always, first byte of data transfer.

## Slide 11: First Byte in Data Transfer on the I2C Bus
MSB
ACK
LSB
7 – Bit Slave Address
R / Wr
R/W’
0 – Slave written by Master
1 – Slave read by Master
ACK – Generated by the slave whose address has been output
By Slave

## Slide 13
MASTER
SLAVE

## Slide 14: Acknowledge
The acknowledge takes place after every byte. The acknowledge bit allows the receiver to signal the transmitter that the byte was successfully received and another byte may be sent.
The Acknowledge signal is defined as follows: the transmitter releases the SDA line during the acknowledge clock pulse so the receiver can pull the SDA line LOW and it remains stable LOW during the HIGH period of this clock pulse.
When SDA remains HIGH during 9th clock pulse, this is defined as the Not Acknowledge signal. The master can then generate either a STOP condition to abort the transfer, or a repeated START condition to start a new transfer.

## Slide 15: Repeated START (Sr) Condition
Instead of the STOP condition, the master can generate a repeated START (Sr) condition.
Like a START condition, to generate a repeated START condition, the master changes the SDA line from one to zero while the SCL line is HIGH
source:DNLWARE

## Slide 16: APB-I2C BRIDGE